## Slide 1
CENIC Voice Services Offering
Level 3’s presentation to VOIP Advisory Committee Review

## Slide 2: Agenda
Corporate Overview
Voice Service Experience
CENIC Product Request/Requirements
Level 3 Solution Overview
Level 3 Architecture
SIP Trunking Design
SIP-PRI Design
IP Centrex Design
Billing Overview
Web Portal

## Slide 3
Headquarters: Broomfield, CO
2009 Annual Revenue: $3.8B
Fortune 500 company
Employees: 5,500
Future Proof Network
One integrated network for SIP and TDM (PRI, Digital Trunk/CAS), for local and long distance
  Built as one solution that is easier and more cost-effective to manage
  Evolutionary approach to leverage existing TDM assets with a clear migration path to SIP as needs evolve
  Built to use existing assets but also to migrate to new ones as needed
Support all communications as they converge over an IP network
  Built for the future
Corporate Overview
54,000 Global long haul route miles
27,000 U.S. metro network miles
Largest IP backbone provider in US
Network Reach

## Slide 4
Traditional Voice Network (Excluding VoIP Network)
  Operate 98 TDM Voice Switches
  More than 48,000 traditional voice circuits (PRIs) in service today
  Supports all standard signaling protocols for voice
Overall Voice Statistics
  Underlying provider to over 40 million end users
  TDM voice leader, carrying over 8 billion minutes per month
  VoIP leader, telephone numbers covering over 83% of U.S. households
Voice Service Experience

## Slide 5: CENIC Product Request/Requirements
Solutions CENIC requested to offer:
  SIP Trunking
  IP Centrex
Level 3 has also suggested:
  PRI delivery via a media gateway
CENICS Solutions Requirements:
  Minimal management of products from a technical and billing solutions
  Utilization of CENIC’s data network
  Ability for universities to be able to manage themselves

## Slide 6: Level 3 Solution Overview
Leverage CENIC’s Network
Offer savings from traditional services by removing the local loop costs
CENIC’s Members can take advantage of purchasing services in quantity as a group
CENIC purchases as the Network Provider
Retains overall control, management and maintenance of the service
Outsources specific skill sets and expertise
Maximizing benefits from existing network investment
Goals
Reduce CAPEX and barriers to entry
Reduce required OPEX to manage services
Create scale increasing discounts

## Slide 7: Level 3 Architecture
Level 3
Feature Servers
AS
MS
SBC
SBC
SBC
SBC
CENIC 10Gb HSIP
SBC
IP PBX
PRI
PBX
IP CENTREX
SIP TRUNKING
SIP TO PRI
Level 3
TDM Network
SBC

## Slide 8: SIP Trunking Design
Level 3
SBC
CENIC
SBC
Campus
SBC
Level 3 will provide SIP Trunking without any additional feature packs to CENIC’s SBCs. Within BroadSoft CENIC will be provisioned as a Service Provider. Universities will be provisioned as an Enterprise and Campuses as a Group. This will increase the level of provisioning CENIC can do themselves without support from the account team and provisioning.
CENIC will receive signaling from Level 3 and will need to identify where to send traffic to via DID range, domain or SIP realm. CENIC would have a SIP peer with each university. CENIC would create a profile for each peer similar to Level 3’s ACME configuration to provide a support for different vendor equipment. ACME Packets professional services can be used to provide support for turning up new SIP peers. This will be a carrier class SBC from ACME.
The campus SBC will solely function as a security device since CENIC is a public network and most IP PBX’s security requires a private IP. This will be a smaller enterprise SBC from ACME.
Campus
IP PBX
The campus IP PBX will signal with the Campus SBC. The university will be required to provide management of the IP PBX.

## Slide 9: SIP-PRI Design
Level 3
SBC
CENIC
SBC
SIP-PRI
Gateway
Level 3 will provide SIP Trunking without any additional feature packs to CENIC’s SBCs. The configuration for this solution will be the same as SIP Trunking since we are only providing IP termination to CENIC.
CENIC will receive signaling from Level 3 and will need to identify where to send traffic to via DID range, domain or SIP realm. CENIC would have a SIP peer with the PRI Gateway. Engineering work will be reduced by standardizing on a PRI gateway (likely Cisco) and be easily reproduced. A public IP address can be used since the gateway can support ACL’s, SIP AUTH and has minimal security concerns as a hardened device.
The PRI gateway (Likely a 2800/3800 series Cisco router) will have a SIP peer with CENIC’s SBC. A basic dial plan will send all traffic to CENIC’s SBC. The Cisco 2800/3800 routers support multiple T1/ISDN/PRI signaling types.
Campus
TDM PBX
The campus PBX would connect to the SIP-PRI gateway in the same way it would to a traditional MPOE. The campus should see no difference in services.

## Slide 10: IP Centrex Design
Level 3
SBC
CENIC
SBC
Campus
SBC
Level 3 will provide a SIP Trunk to CENIC’s ACME… DID’s will be assigned feature packs to provide voicemail, call forwarding, etc.. like a traditional IP Centrex service with the exception of the phones will not register to Level 3’s SBC’s.
CENIC will receive the SIP traffic and parse it to the correct campus SBC via a defined field such as DID, SIP realm or SIP Domain. This allows CENIC to provide a mid-level of management but, does not require CENIC to maintain a user database and/or manage handsets.
The Campus SBC will maintain a local user database (LDAP) connecting to the SBC via radius. Authenticated users will be mapped to the correct rule via a translation. This will most likely require some of the digits from the DID to be part of the SIP username.
IP Phone
IP Phones will be registered to the campus SBC where calls are being translated to the correct handset. Advanced PBX features are provided in the cloud by the Level 3 feature packs. Handset configuration and management can be handled by an XML generating application from the LDAP DB.

## Slide 11: Billing Overview
Billing is possible by location, campus or university
Flat Rates for LD and Local
  Dorms may be an exception due to calling patterns
    Level 3 would need to evaluate flat rate dorm prices on individual case basis
  International Calls can be billed back to each telephone number
E-Rate Team available to assist
Offering is Open to All CENIC Members and Partners

## Slide 12: Web Portal
Multiple level of management
  Service Provider, Enterprise, Group
Optional direct end-user login
  Manage DID based features such as call forwarding, voicemail, time of day rules
  Reduces helpdesk requests