## Slide 1: Alpha Contributed SNC-60x0-488F By Robert Chu On September 8, 2018 (For General Review)

## Slide 2: Brief Description of SNC-60x0-488F
48 Ports of 25G SFP28 with 8 ports of 100G QSFP 28 Leaf Switch for Data Center
This SNC-60x0-488F is for either Enterprise or Carrier TOR switch.
It comes with ONIE and has three different CPU modules- Rangeley, Broadwell DE, and Denverton.

## Slide 3
SNC-60x0-488F
  48 x 25 G SFP28 + 8 x 100G QSFP28

## Slide 4: Product Brief
MAC Solution
  Trident3 2T (BCM56873)
I/O Configuration
  48 x 25G SFP28 + 8 x 100G QSFP28
  Serial console, Ethernet Management Port, USB for Storage
Modular Control Processor Board
  Intel Rangeley
  Intel Broadwell-DE
  Denverton
Resilient Design
  Redundant Power Supply (AC and DC)
  5+1 Hot Pluggable Fans
Specification
  Operation Temperature:
    Front to Back Air Flow (0~45oC)
    Back to Front Air Flow (0~40oC)
Dimension
  441mm (W) X 487.4mm (D) X 44mm (H)

## Slide 5: Enhancement Options
Control Processor Board Options
  Intel Rangeley C2558 Four Cores/2.4GHz
    DDR3 4GB (maximum up to 32GB)
    M.2 SATA SSD 32GB (maximum up to 128GB)
    Boot Flash 8MB (maximum up to 16MB)
  Intel Broadwell-DE D-1518 Four Cores/2.3GHz
    DDR4 8GB (maximum up to 32GB)
    M.2 SATA SSD 32GB (maximum up to 128GB)
    Boot Flash 16MB (maximum up to 32MB)

## Slide 6: Enhancement Options Continued..
Control Processor Board Options
  Intel Denverton C3958 Sixteen Cores/2.0GHz (with an options of 2 to 12 cores. Refer to the Appendix for more information.)
    DDR4 16GB * 2 (maximum up to 32GB) (with C3338 supporting only one 16GB)
    M.2 SATA SSD 64GB
    Boot Flash 32MB
    eMMC 16GB (reserved up to 32GB)
    TPM is optional
TPM (Trusted Platform Module)
  Nuvoton NPCT650

## Slide 7: Main Board Diagram
Notes: The SerDes is code-named as Falcon Core (32 of them.)
For 25g, with 56873 it can provide up to 80 SerDes lanes.

## Slide 8: CPU board

## Slide 9: Front Panel

## Slide 10: Rear View

## Slide 11: Chassis Dimensional Drawing

## Slide 12: Top View

## Slide 13: Different CPUs with its Management Ethernet Port

## Slide 14: Some LED’s Definition

## Slide 15: More of some LED’s definition

## Slide 16: Some Regulatory Complianc

## Slide 17: Other Reports Available

## Slide 18: Take Home
SNC-60x0-448F is a Trident 3 switch for Enterprise and Data Center.
It provides 25G downlink and 100G uplink.
There are three CPUs supported in this switch. They are: a)Rangeley, b) Broadwell DE, and c) Denverton.
It comes with ONIE support.

## Slide 19
Appendix

## Slide 20: The Family of Denverton Supported

## Slide 21: Some CPU Pin-out

## Slide 22: Front panel picture

## Slide 23: Alpha Recommends Cables for “Insert and Release” on Ports