# FSH Broadband Network Feasibility Project

Charge:  To implement broadband network service to FSH by Fall 2003 at an acceptable cost.

The following is a summary of research that was conducted regarding:

- off-campus ISP services and on-campus connectivity options for the Family Student Housing residential area;

- financial analysis for viable options; and

- the CUHS IT recommendation.

Section 1 – Connectivity Options

- Off-campus ISP services (consideration of non-UCSC students, staff, or faculty using UCSC network resources).

- DSL -- SBC has confirmed that they are unwilling to place the necessary equipment at FSH to provide this service even if CUHS were to incur the capital costs associated with the project.

- Cable -- Area cable providers are unable to provide broadband cable service at this time

- Satellite & Wireless -- Satellite DSL is a high-cost, equipment intensive solution that is still developing and is not yet reliable.  Wireless is a difficult solution for FSH due to the complex topography and terrain.  CATS Network Engineers have agreed that this is not a good primary solution for FSH at this time.  In the future as wireless technology improves, this may become a possible secondary option for FSH.

- On-campus connectivity

  - Option 1.  Cable Broadband Access (See Budget Attachment, pg. 2)

Pros

    - Phase-in implementation possible by Fall Quarter 2003 with completion by December 2003

    - Reasonable implementation cost

    - Uses pre-existing cable network wiring that does not need to be upgraded

    - CATS and Media Services have agreed to work together to develop a comprehensive service model

    - Connects to Campus Residential Network

Cons

    - Cable technology requires a sharing of the maximum network bandwidth (ethernet is individual lines)

    - New methodology for our campus therefore they will be a learning curve for infrastructure and support

      - Fiber to buildings and CAT5 wiring within buildings in the FSH Community (See Budget Attachment, pg. 3)

Pros

        - Provides current technology maximum bandwidth service to each port

        - Utilizes current staff/vendor infrastructure and support technology

Cons

- Implementation would involve close coordination with FSH Renovation project which could produce significant delays and additional inconvenience to residents

- High cost per port

- Equipment Intensive solution with corresponding ongoing replacement schedule

  - Maintain current network dial-up model

Pros

    - No Cost

    - Awaits technology and other options

Cons

- Does not fulfill any aspect of charge

# FSH Community requests more service

# Section 2 – Financial Analysis of Viable Options

# Option1 Budget -- Fiber & CAT5 Wiring

Provided that there are 40 buildings within the FSH Complex, a ballpark Fiber/CAT 5 estimate would give the following numbers:

| Description | Initial Investment | Annual Ongoing Cost |
| --- | --- | --- |
| Fiber wiring ($11,000/building) | $440,000 |  |
| Building Wiring ($3,000/building) | $120,000 |  |
| Network Equipment($4,000/building) | $160,000 | $32,000 |
| Bandwidth |  | $10,000 |
| ResNet Support |  | $5,000 |
| 10% Project Engineering Cost | $72,000 |  |
| 10% Project Management Cost | $72,000 |  |
| Total | $864,000 | $47,000 |

# Given that this number assumes many details that would ordinarily be determined by an onsite cable engineer, the estimate is not supported by CATS or CUHS IT.  A comprehensive analysis is available from SFM, the original contractor for the previous SCS upgrades, for a $10,000 fee.

# Option 2 Budget -- Cable Broadband Access

## CATS Network Support	Initial Investment	Annual Ongoing Cost

| Training | $7,500 | $3,000 |
| --- | --- | --- |
| Bandwidth |  | $10,000 |
| Technical Support, Diagnostics, Monitoring |  | $10,000 |
| Conduit Run | $40,000 |  |
| Network Electronics | $30,000 | $6,000 |
| TOTAL | $77,500 | $29,000 |
| Media Services Cable Support |  |  |
| Leakage Detector | $2,000 |  |
| Training | $7,500 | $3,000 |
| Technical Support |  | $10,000 |
| Amplifier Replacement | $3,000 | $300 |
| Hardline Tap Replacement | $2,000 |  |
| TOTAL | $14,500 | $13,300 |
| FSH Residential Network Support |  |  |
| Test Equipment | $6,000 | $1,500 |
| Training | $1,000 |  |
| Cable Modem | $30,000 | $6,000 |
| Technical Help, Publications, Contracts, etc. |  | $4,000 |
| Staff Support (12mos) |  | $30,000 |
| Tier 2 Support (ResNet) |  | $5,000 |
| TOTAL | $37,000 | $46,500 |
| Estimated Project Grand Total | $129,000 | $88,800 |

Section 3 -- CUHS IT Recommendation

The charge given to CUHS IT included the following criteria:

- A solution ready for implementation by Fall 2003

- Broadband network service available to all residents

- Greatest broadband service potential at the lowest cost to Family Student Housing residents

Working within these parameters, IT recommends that CUHS proceed with Option 2 – Cable Broadband Access.